## Slide 1: ECE-2002 Computer Organization and Architecture
Dr. Kritika Bansal
School of Electronics Engineering, VIT-AP

## Slide 2
ADD and SUB Instructions
The ADD/SUB instruction can take place between −
Register to register
Memory to register
Register to memory
Register to constant data
Memory to constant data
Memory-to-memory operations are not possible using ADD/SUB instructions.

## Slide 3
MUL/IMUL Instructions
Multiplicand in both cases will be in an accumulator.

## Slide 4
MUL/IMUL Instructions

## Slide 5
DIV/IDIV Instructions
The dividend is in an accumulator.

## Slide 6
Write an assembly language program to compute Y=(A+B)*C+(A-B)*D
A is stored in 2000
B is stored in 2002
C is stored in 2004
D is stored in 2006
Store Y in 3000

## Slide 7
Write an assembly language program to compute Y=(A+B)*C+(A-B)*D
MOV AX, [2000]
MOV BX, [2002]
ADD AX, BX
MOV [5000], AX
MOV AX, [2000]
SUB AX, BX
MOV [5002], AX
MOV AX, [2004]
MUL [5000]
MOV [6000], AX
MOV AX, [2006]
MUL [5002]
MOV [6002], AX
MOV AX, [6000]
ADD AX, [6002]
MOV [3000], AX
HLT
A is stored in 2000
B is stored in 2002
C is stored in 2004
D is stored in 2006
Store Y in 3000

## Slide 8
Write an assembly language program to compute Y=(A-B)/(C+(D*E))
A is stored in 2000
B is stored in 2002
C is stored in 2004
D is stored in 2006
E is stored in 2008
Store Y in 3000

## Slide 9
Write an assembly language program to
Add two 8-bit numbers
Add two 16-bit numbers

## Slide 10
Write an assembly language program to
Add two 8-bit numbers with or without carry
Add two 16-bit numbers with or without carry

## Slide 11
Write an assembly language program to add two 8-bit numbers with or without carry
MOV CL, 00
MOV AL, [2000]
MOV BL, [2001]
ADD AL, BL
    JNC LOOP
    INC CL
LOOP MOV [2002], AL
MOV [2003], CL
HLT
1st number in 2000
2nd number in 2001
Store result in 2002
Store carry in 2003

## Slide 12
Write an assembly language program to add two 16-bit numbers with or without carry
MOV CX, 0000
MOV AX, [2000]
MOV BX, [2002]
ADD AX, BX
    JNC LOOP
    INC CX
LOOP MOV [2004], AX
MOV [2006], CX
HLT

## Slide 13
Write an assembly language program to
Subtract two 8-bit numbers with or without borrow
Subtract two 16-bit numbers with or without borrow

## Slide 14
Write an assembly language program to multiply two 16-bit numbers where starting address is 1000 and the numbers are at 2000 and 2002 memory address and store result into 2004 and 2006 memory address.

## Slide 15
Write an assembly language program to multiply two 16-bit numbers
MOV AX, [2000]
MOV BX, [2002]
MUL BX
MOV [2004], AX
MOV AX, DX
MOV [2006], AX
HLT